## Slide 1
URBANSENSE
Structural Pulse — Continuous bridge-health screening using the buses already crossing the city.
SIH 2026 • PS 26124 BEL • Smart Automation • Theme: Mobile Urban Intelligence
Buses as mobile structural sensors
Not collapse prediction — flag for inspection
One bus → many intelligences
PUBLIC BUS
↓
↓
↓
Camera
Road defects
GPS
Location
IMU
Vibration
↓
URBANSENSE → Fusion (spatial + source diversity)
Road condition Potholes, waterlogging, missing assets
Structure health ★ Bridge / ROB / Flyover screening

## Slide 2
Problem → why buses?
India has a huge inventory of bridges/ROBs/flyovers. Fixed instrumentation on every structure is expensive.
Today (others):
bus camera → pothole → dashboard (camera carrier only)
Cost: 10–20L per bridge for fixed SHM
Gap: Periodic inspection → visible deterioration tak pata hi nahi chalta. Research: vehicle dynamics / road-profile / sensor noise are major issues — one pass ≠ diagnosis.
Our jump:
What if the bus can also sense the health of the infrastructure it physically travels over?
Fleet already traverses structures → temporary sensing nodes
Benefit: Network-level screening without installing on every structure. BEL relevant: electronics + sensor signal processing.

## Slide 3
Structural Pulse — Sense • Learn • Flag (not collapse prediction)
Continuous screening → inspection recommendation
SENSE
Smartphone IMU (50Hz) + GPS records bridge-crossing dynamics 70m geofence, 1–3s batch
LEARN
Per-structure EMA baseline f_dom + RMS + crest Longitudinal history 80 pts
FLAG
Persistent drift across buses → ANOMALOUS Auto WO-BR-* + inspection
Correct claim: “This bridge's observed dynamic response has changed enough from its baseline to warrant inspection.” • Screening layer, not certified inspection.

## Slide 4
Architecture — one observation stream, not a separate product
BUS
CAMERA Road AI → pothole
GPS Location + speed + direction
IMU Vibration → RMS/peak/crest + FFT f_dom
└───────────────┼───────────────┘
↓ OBSERVATION (phone accel + GPS, ~1KB JSON, ~1.6s on bridge)
URBAN FUSION (spatial + temporal + source diversity)
↓
STRUCTURE / ROAD STATE → Health score • Work Order • GIS map
One bus tells: road deteriorating + bridge anomalous + traffic rising + pedestrian high
Per-structure asset: BRIDGE-DEL-042 • dynamic baseline (f_dom, RMS, spectral) • environmental (speed, direction, time) • state NORMAL→WATCH→ANOMALOUS→INSPECTION REQUIRED
Reuse: Observation → Fusion → UrbanEvent • No new platform. DOPT safe: no face/plate, only vibration.

## Slide 5
Demo loop — 60 days in 60 seconds (killer version)
DAY 1
BUS-017
Bridge X
↓ Acceleration signature ↓
Baseline
Baseline created
DAY 14
BUS-042
Bridge X
↓ Acceleration signature ↓
Matches
Matches baseline
DAY 60
BUS-017/042/103
Bridge X
↓ Acceleration signature ↓
Repeated measurements
Statistically significant drift ⚠ STRUCTURAL ANOMALY → Inspection
The word DRIFT is important — we never claim ‘will collapse’.
Judge Q: ‘Why buses vs sensors on bridge?’ → ‘Not another network to maintain. Fleet already crosses daily — network-scale without installing on every structure.’ Judge Q: ‘Bridge vs bus?’ → Control for direction/speed + persistent across buses.

## Slide 6
Why this wins — honest scores
Impact
9.5/10
Fit with PS
9.5/10
Technical depth
9/10
BEL relevance
9/10
Demo potential
9/10
System novelty
8.5/10
Science novelty 5/10 — drive-by SHM exists (2023 IoT, 2026 smartphone modal). Our novelty = fleet-scale screening as one layer of urban intelligence.
Warning: Build screening demonstrator (2–3 phones same flyover → f_dom/RMS → GIS yellow/red), not collapse proof.